Purpose:	All employees, supervisors, and members of management, understand the importance of fall protection; when to use it, how to use it, and how to prevent hazardous conditions that could result in slips, trips or falls.

Scope:	                            Applicable to all Company Name Here locations.

Citation:	             29 CFR 1926.500

Note – any references made to paragraphs or sections are of the OSHA standard itself; not of this policy.

DEFINITIONS:

Anchorage means a secure point of attachment for lifelines, lanyards or deceleration devices.

Body belt (safety belt) means a strap with means both for securing it about the waist and for attaching it to a lanyard, lifeline, or deceleration device.

Body harness means straps which may be secured about the employee in a manner that will distribute the fall arrest forces over at least the thighs, pelvis, waist, chest and shoulders with means for attaching it to other components of a personal fall arrest system.

Buckle means any device for holding the body belt or body harness closed around the employee's body.

Connector means a device which is used to couple (connect) parts of the personal fall arrest system and positioning device systems together. It may be an independent component of the system, such as a carabineer, or it may be an integral component of part of the system (such as a buckle or dee-ring sewn into a body belt or body harness, or a snap-hook spliced or sewn to a lanyard or self-retracting lanyard).

Controlled access zone (CAZ) means an area in which certain work (e.g., overhand bricklaying) may take place without the use of guardrail systems, personal fall arrest systems, or safety net systems and access to the zone is controlled.

Dangerous equipment means equipment (such as pickling or galvanizing tanks, degreasing units, machinery, electrical equipment, and other units) which, as a result of form or function, may be hazardous to employees who fall onto or into such equipment.

Deceleration device means any mechanism, such as a rope grab, rip-stitch lanyard, specially-woven lanyard, tearing or deforming lanyards, automatic self-retracting lifelines/lanyards, etc., which serves to dissipate a substantial amount of energy during a fall arrest, or otherwise limit the energy imposed on an employee during fall arrest.

Deceleration distance means the additional vertical distance a falling employee travels, excluding lifeline elongation and free fall distance, before stopping, from the point at which the deceleration device begins to operate. It is measured as the distance between the location of an employee's body belt or body harness attachment point at the moment of activation (at the onset of fall arrest forces) of the deceleration device during a fall, and the location of that attachment point after the employee comes to a full stop.

Equivalent means alternative designs, materials, or methods to protect against a hazard which Company Name Here can demonstrate will provide an equal or greater degree of safety for employees than the methods, materials or designs specified in the standard.

Failure means load refusal, breakage, or separation of component parts. Load refusal is the point where the ultimate strength is exceeded.

Free fall means the act of falling before a personal fall arrest system begins to apply force to arrest the fall.

Free fall distance means the vertical displacement of the fall arrest attachment point on the employee's body belt or body harness between onset of the fall and just before the system begins to apply force to arrest the fall. This distance excludes deceleration distance, and lifeline/lanyard elongation, but includes any deceleration device slide distance or self-retracting lifeline/lanyard extension before they operate and fall arrest forces occur.

Guardrail system means a barrier erected to prevent employees from falling to lower levels.

Hole means a gap or void 2 inches (5.1 cm) or more in its least dimension, in a floor, roof, or other walking/working surface.

Infeasible means that it is impossible to perform the construction work using a conventional fall protection system (i.e., guardrail system, safety net system, or personal fall arrest system) or that it is technologically impossible to use any one of these systems to provide fall protection.

Lanyard means a flexible line of rope, wire rope, or strap which generally has a connector at each end for connecting the body belt or body harness to a deceleration device, lifeline, or anchorage.

Leading edge means the edge of a floor, roof, or formwork for a floor or other walking/working surface (such as the deck) which changes location as additional floor, roof, decking, or formwork sections are placed, formed, or constructed. A leading edge is considered to be an "unprotected side and edge" during periods when it is not actively and continuously under construction.

Lifeline means a component consisting of a flexible line for connection to an anchorage at one end to hang vertically (vertical lifeline), or for connection to anchorages at both ends to stretch horizontally (horizontal lifeline), and which serves as a means for connecting other components of a personal fall arrest system to the anchorage.

Low-slope roof means a roof having a slope less than or equal to 4 in 12 (vertical to horizontal).

Lower levels mean those areas or surfaces to which an employee can fall. Such areas or surfaces include, but are not limited to, ground levels, floors, platforms, ramps, runways, excavations, pits, tanks, material, water, equipment, structures or portions thereof.

Mechanical equipment means all motor or human propelled wheeled equipment used for roofing work, except wheelbarrows and mop carts.

Openings means a gap or void 30 inches (76 cm) or more high and 18 inches (48 cm) or more wide, in a wall or partition, through which employees can fall to a lower level.

Overhand bricklaying and related work means the process of laying bricks and masonry units such that the surface of the wall to be jointed is on the opposite side of the wall from the mason, requiring the mason to lean over the wall to complete the work. Related work includes mason tending and electrical installation incorporated into the brick wall during the overhand bricklaying process.

Personal fall arrest system means a system used to arrest an employee in a fall from a working level. It consists of an anchorage, connectors, a body belt or body harness and may include a lanyard, deceleration device, lifeline, or suitable combinations of these. As of January 1, 1998, the use of a body belt for fall arrest is prohibited.

Positioning device system means a body belt or body harness system rigged to allow an employee to be supported on an elevated vertical surface, such as a wall, and work with both hands free while leaning.

Rope grab means a deceleration device which travels on a lifeline and automatically, by friction, engages the lifeline and locks so as to arrest the fall of an employee. A rope grab usually employs the principle of inertial locking, cam/level locking, or both.

Roof means the exterior surface on the top of a building. This does not include floors or formwork which, because a building has not been completed, temporarily becomes the top surface of a building.

Roofing work means the hoisting, storage, application, and removal of roofing materials and equipment, including related insulation, sheet metal, and vapor barrier work, but not including the construction of the roof deck.

Safety-monitoring system means a safety system in which a competent person is responsible for recognizing and warning employees of fall hazards.

Self-retracting lifeline/lanyard means a deceleration device containing a drum-wound line which can be slowly extracted from, or retracted onto, the drum under slight tension during normal employee movement, and which, after onset of a fall, automatically locks the drum and arrests the fall.

Snap hook means a connector comprised of a hook-shaped member with a normally closed keeper, or similar arrangement, which may be opened to permit the hook to receive an object and, when released, automatically closes to retain the object. Snap hooks are generally one of two types:

The locking type with a self-closing, self-locking keeper which remains closed and locked until unlocked and pressed open for connection or disconnection; or

The non-locking type with a self-closing keeper which remains closed until pressed open for connection or disconnection. As of January 1, 1998, the use of a non-locking snap hook as part of personal fall arrest systems and positioning device systems is prohibited.

Steep roof means a roof having a slope greater than 4 in 12 (vertical to horizontal).

Toe board means a low protective barrier that will prevent the fall of materials and equipment to lower levels and provide protection from falls for personnel.

Unprotected sides and edges means any side or edge (except at entrances to points of access) of a walking/working surface, e.g., floor, roof, ramp, or runway where there is no wall or guardrail system at least 39 inches (1.0 m) high.

Walking/working surface means any surface, whether horizontal or vertical on which an employee walks or works, including, but not limited to, floors, roofs, ramps, bridges, runways, formwork and concrete reinforcing steel but not including ladders, vehicles, or trailers, on which employees must be located in order to perform their job duties.

Warning line system means a barrier erected on a roof to warn employees that they are approaching an unprotected roof side or edge, and which designates an area in which roofing work may take place without the use of guardrail, body belt, or safety net systems to protect employees in the area.

Work area means that portion of a walking/working surface where job duties are being performed.

“General”

This section sets forth requirements for Company Name Here to provide fall protection systems. All fall protection required by this section will conform to the criteria set forth in 1926.502 of this subpart.

Company Name Here will determine if the walking/working surfaces on which its employees are to work have the strength and structural integrity to support employees safely. Employees will be allowed to work on those surfaces only when the surfaces have the requisite strength and structural integrity.

"Unprotected sides and edges."

Each employee on a walking/working surface (horizontal and vertical surface) with an unprotected side or edge which is 6 feet (1.8 m) or more above a lower level will be protected from falling by the use of guardrail systems, safety net systems, or personal fall arrest systems.

"Leading edges."

Each employee who is constructing a leading edge 6 feet (1.8 m) or more above lower levels will be protected from falling by guardrail systems, safety net systems, or personal fall arrest systems. Exception: When Company Name Here can demonstrate that it is infeasible or creates a greater hazard to use these systems, Company Name Here will develop and implement a fall protection plan which meets the requirements of paragraph (k) of 1926.502.

Note: There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the above-listed fall protection systems. Accordingly, Company Name Here has the burden of establishing that it is appropriate to implement a fall protection plan which complies with 1926.502(k) for a particular workplace situation, in lieu of implementing any of those systems.

Each employee on a walking/working surface 6 feet (1.8 m) or more above a lower level where leading edges are under construction, but who is not engaged in the leading edge work, will be protected from falling by a guardrail system, safety net system, or personal fall arrest system. If a guardrail system is chosen to provide the fall protection, and a controlled access zone has already been established for leading edge work, the control line may be used in lieu of a guardrail along the edge that parallels the leading edge.

"Hoist areas."

Each employee in a hoist area will be protected from falling 6 feet (1.8 m) or more to lower levels by guardrail systems or personal fall arrest systems. If guardrail systems, [or chain, gate, or guardrail] or portions thereof, are removed to facilitate the hoisting operation (e.g., during landing of materials), and an employee must lean through the access opening or out over the edge of the access opening (to receive or guide equipment and materials, for example), that employee will be protected from fall hazards by a personal fall arrest system.

"Holes."

Each employee on walking/working surfaces will be protected from falling through holes (including skylights) more than 6 feet (1.8 m) above lower levels, by personal fall arrest systems, covers, or guardrail systems erected around such holes.

Each employee on a walking/working surface will be protected from tripping in or stepping into or through holes (including skylights) by covers.

Each employee on a walking/working surface will be protected from objects falling through holes (including skylights) by covers.

"Formwork and reinforcing steel."

Each employee on the face of formwork or reinforcing steel will be protected from falling 6 feet (1.8 m) or more to lower levels by personal fall arrest systems, safety net systems, or positioning device systems.

"Ramps, runways, and other walkways."

Each employee on ramps, runways, and other walkways will be protected from falling 6 feet (1.8 m) or more to lower levels by guardrail systems.

"Excavations."

Each employee at the edge of an excavation 6 feet (1.8 m) or more in depth will be protected from falling by guardrail systems, fences, or barricades when the excavations are not readily seen because of plant growth or other visual barrier;

Each employee at the edge of a well, pit, shaft, and similar excavation 6 feet (1.8 m) or more in depth will be protected from falling by guardrail systems, fences, barricades, or covers.

"Dangerous equipment."

Each employee less than 6 feet (1.8 m) above dangerous equipment will be protected from falling into or onto the dangerous equipment by guardrail systems or by equipment guards.

Each employee 6 feet (1.8 m) or more above dangerous equipment will be protected from fall hazards by guardrail systems, personal fall arrest systems, or safety net systems.

"Overhand bricklaying and related work."

Except as otherwise provided in paragraph (b) of this section, each employee performing overhand bricklaying and related work 6 feet (1.8 m) or more above lower levels, will be protected from falling by guardrail systems, safety net systems, personal fall arrest systems, or will work in a controlled access zone.

Each employee reaching more than 10 inches (25 cm) below the level of the walking/working surface on which they are working will be protected from falling by a guardrail system, safety net system, or personal fall arrest system.

Note: Bricklaying operations performed on scaffolds are regulated by subpart L - Scaffolds of this part.

"Roofing works on Low-slope roofs."

Except as otherwise provided in paragraph (b) of this section, each employee engaged in roofing activities on low-slope roofs, with unprotected sides and edges 6 feet (1.8 m) or more above lower levels will be protected from falling by guardrail systems, safety net systems, personal fall arrest systems, or a combination of warning line system and guardrail system, warning line system and safety net system, or warning line system and personal fall arrest system, or warning line system and safety monitoring system. Or, on roofs 50-feet (15.25 m) or less in width (see Appendix A to subpart M of this part), the use of a safety monitoring system alone [i.e. without the warning line system] is permitted.

"Steep roofs."

Each employee on a steep roof with unprotected sides and edges 6 feet (1.8 m) or more above lower levels will be protected from falling by guardrail systems with toeboards, safety net systems, or personal fall arrest systems.

"Precast concrete erection."

Each employee engaged in the erection of precast concrete members (including, but not limited to the erection of wall panels, columns, beams, and floor and roof "tees") and related operations such as grouting of precast concrete members, who is 6 feet (1.8 m) or more above lower levels will be protected from falling by guardrail systems, safety net systems, or personal fall arrest systems, unless another provision in paragraph (b) of this section provides for an alternative fall protection measure. Exception: When Company Name Here can demonstrate that it is infeasible or creates a greater hazard to use these systems, Company Name Here will develop and implement a fall protection plan which meets the requirements of paragraph (k) of 1926.502.

Note: There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the above-listed fall protection systems. Accordingly, Company Name Here has the burden of establishing that it is appropriate to implement a fall protection plan which complies with 1926.502(k) for a particular workplace situation, in lieu of implementing any of those systems.

"Residential construction."

Each employee engaged in residential construction activities 6 feet (1.8 m) or more above lower levels will be protected by guardrail systems, safety net system, or personal fall arrest system unless another provision in paragraph (b) of this section provides for an alternative fall protection measure. Exception: When Company Name Here can demonstrate that it is infeasible or creates a greater hazard to use these systems, Company Name Here will develop and implement a fall protection plan which meets the requirements of paragraph (k) of 1926.502.

Note: There is a presumption that it is feasible and will not create a greater hazard to implement at least one of the above-listed fall protection systems. Accordingly, Company Name Here has the burden of establishing that it is appropriate to implement a fall protection plan which complies with 1926.502(k) for a particular workplace situation, in lieu of implementing any of those systems.

"Wall openings."

Each employee working on, at, above, or near wall openings (including those with chutes attached) where the outside bottom edge of the wall opening is 6 feet (1.8 m) or more above lower levels and the inside bottom edge of the wall opening is less than 39 inches (1.0 m) above the walking/working surface, will be protected from falling by the use of a guardrail system, a safety net system, or a personal fall arrest system.

"Walking/working surfaces not otherwise addressed."

Except as provided in 1926.500(a)(2) or in 1926.501 (b)(1) through (b)(14), each employee on a walking/working surface 6 feet (1.8 m) or more above lower levels will be protected from falling by a guardrail system, safety net system, or personal fall arrest system.

"Protection from falling objects."

When an employee is exposed to falling objects, Company Name Here will have each employee wear a hard hat and will implement one of the following measures:

Erect toe boards, screens, or guardrail systems to prevent objects from falling from higher levels; or,

Erect a canopy structure and keep potential fall objects far enough from the edge of the higher level so that those objects would not go over the edge if they were accidentally displaced; or,

Barricade the area to which objects could fall, prohibit employees from entering the barricaded area, and keep objects that may fall far enough away from the edge of a higher level so that those objects would not go over the edge if they were accidentally displaced.

"General."

Fall protection systems required by this part will comply with the applicable provisions of this section.

Company Name Here will provide and install all fall protection systems required by this subpart for an employee, and will comply with all other pertinent requirements of this subpart before that employee begins the work that necessitates the fall protection.

"Guard rail systems."

Guardrail systems and their use will comply with the following provisions:

Top edge height of top rails, or equivalent guardrail system members, will be 42 inches (1.1 m) plus or minus 3 inches (8 cm) above the walking/working level. When conditions warrant, the height of the top edge may exceed the 45-inch height, provided the guardrail system meets all other criteria of this paragraph.

Note: When employees are using stilts, the top edge height of the top rail, or equivalent member, will be increased an amount equal to the height of the stilts.

Mid rails, screens, mesh, intermediate vertical members, or equivalent intermediate structural members will be installed between the top edge of the guardrail system and the walking/working surface when there is no wall or parapet wall at least 21 inches (53 cm) high.

Mid rails, when used, will be installed at a height midway between the top edge of the guardrail system and the walking/working level.

Screens and mesh, when used, will extend from the top rail to the walking/working level and along the entire opening between top rail supports.

Intermediate members (such as balusters), when used between posts, will be not more than 19 inches (48 cm) apart.

Other structural members (such as additional midrails and architectural panels) will be installed such that there are no openings in the guardrail system that are more than 19 inches (.5 m) wide.

Guard rail systems will be capable of withstanding, without failure, a force of at least 200 pounds (890 N) applied within 2 inches (5.1 cm) of the top edge, in any outward or downward direction, at any point along the top edge.

When the 200 pound (890 N) test load specified in paragraph (b)(3) of this section is applied in a downward direction, the top edge of the guardrail will not deflect to a height less than 39 inches (1.0 m) above the walking/working level. Guardrail system components selected and constructed in accordance with the Appendix B to subpart M of this part will be deemed to meet this requirement.

Mid rails, screens, mesh, intermediate vertical members, solid panels, and equivalent structural members will be capable of withstanding, without failure, a force of at least 150 pounds (666 N) applied in any downward or outward direction at any point along the mid rail or other member.

Guardrail systems will be so surfaced as to prevent injury to an employee from punctures or lacerations, and to prevent snagging of clothing.

The ends of all top rails and mid rails will not overhang the terminal posts, except where such overhang does not constitute a projection hazard.

Steel banding and plastic banding will not be used as top rails or mid rails.

Top rails and mid rails will be at least one-quarter inch (0.6 cm) nominal diameter or thickness to prevent cuts and lacerations. If wire rope is used for top rails, it will be flagged at not more than 6-foot intervals with high-visibility material.

When guardrail systems are used at hoisting areas, a chain, gate or removable guardrail section will be placed across the access opening between guardrail sections when hoisting operations are not taking place.

When guardrail systems are used at holes, they will be erected on all unprotected sides or edges of the hole.

When guardrail systems are used around holes used for the passage of materials, the hole will have not more than two sides provided with removable guardrail sections to allow the passage of materials. When the hole is not in use, it will be closed over with a cover, or a guardrail system will be provided along all unprotected sides or edges.

When guardrail systems are used around holes which are used as points of access (such as ladderways), they will be provided with a gate, or be so offset that a person cannot walk directly into the hole.

Guardrail systems used on ramps and runways will be erected along each unprotected side or edge.

Manila, plastic or synthetic rope being used for top rails or mid rails will be inspected as frequently as necessary to ensure that it continues to meet the strength requirements of paragraph (b)(3) of this section.

"Personal fall arrest systems."

Personal fall arrest systems and their use will comply with the provisions set forth below. Effective January 1, 1998, body belts are not acceptable as part of a personal fall arrest system. Note: The use of a body belt in a positioning device system is acceptable and is regulated under paragraph (e) of this section.

Connectors will be drop forged, pressed or formed steel, or made of equivalent materials.

Connectors will have a corrosion-resistant finish, and all surfaces and edges will be smooth to prevent damage to interfacing parts of the system.

Dee-rings and snap hooks will have a minimum tensile strength of 5,000 pounds (22.2 kN).

Dee-rings and snap hooks will be proof-tested to a minimum tensile load of 3,600 pounds (16 k n) without cracking, breaking, or taking permanent deformation.

Snap hooks will be sized to be compatible with the member to which they are connected to prevent unintentional disengagement of the snap hook by depression of the snap hook keeper by the connected member, or will be a locking type snap hook designed and used to prevent disengagement of the snap hook by the contact of the snap hook keeper by the connected member. Effective January 1, 1998, only locking type snap hooks will be used.

Unless the snap hook is a locking type and designed for the following connections, snap hooks will not be engaged:

1. Directly to webbing, rope or wire rope;

2. To each other;

3. To a Dee-ring to which another snap hook or other connector is attached;

4. To a horizontal lifeline; or

5. To any object which is incompatibly shaped or dimensioned in relation to the snap hook                               such that unintentional disengagement could occur by the connected object being able to depress the snap hook keeper and release itself.

On suspended scaffolds or similar work platforms with horizontal lifelines which may become vertical lifelines, the devices used to connect to a horizontal lifeline will be capable of locking in both directions on the lifeline.

Horizontal lifelines will be designed, installed, and used, under the supervision of a qualified person, as part of a complete personal fall arrest system, which maintains a safety factor of at least two.

Lanyards and vertical lifelines will have a minimum breaking strength of 5,000 pounds (22.2 kN).

Except as provided in paragraph (d)(10)(ii) of this section, when vertical lifelines are used, each employee will be attached to a separate lifeline.

During the construction of elevator shafts, two employees may be attached to the same lifeline in the hoist way, provided both employees are working atop a false car that is equipped with guardrails; the strength of the lifeline is 10,000 pounds [5,000 pounds per employee attached] (44.4 kN); and all other criteria specified in this paragraph for lifelines have been met.

Lifelines will be protected against being cut or abraded.

Self-retracting lifelines and lanyards which automatically limit free fall distance to 2 feet (0.61 m) or less will be capable of sustaining a minimum tensile load of 3,000 pounds (13.3 kN) applied to the device with the lifeline or lanyard in the fully extended position.

Self-retracting lifelines and lanyards which do not limit free fall distance to 2 feet (0.61 m) or less, rip stitch lanyards, and tearing and deforming lanyards will be capable of sustaining a minimum tensile load of 5,000 pounds (22.2 kN) applied to the device with the lifeline or lanyard in the fully extended position.

Ropes and straps (webbing) used in lanyards, lifelines, and strength components of body belts and body harnesses will be made from synthetic fibers.

Anchorages used for attachment of personal fall arrest equipment will be independent of any anchorage being used to support or suspend platforms and capable of supporting at least 5,000 pounds (22.2 kN) per employee attached, or will be designed, installed, and used as follows:

1. As part of a complete personal fall arrest system which maintains a safety factor of at least two; and

2. under the supervision of a qualified person.

Personal fall arrest systems, when stopping a fall, will:

1. Limit maximum arresting force on an employee to 900 pounds (4 kN) when used with a body belt;

2. Limit maximum arresting force on an employee to 1,800 pounds (8 kN) when used with a body harness;

3. Be rigged such that an employee can neither free fall more than 6 feet (1.8 m), nor contact any lower level;

4. Bring an employee to a complete stop and limit maximum deceleration distance an employee travels to 3.5 feet (1.07 m); and,

5. Have sufficient strength to withstand twice the potential impact energy of an employee free falling a distance of 6 feet (1.8 m), or the free fall distance permitted by the system, whichever is less.

Note: If the personal fall arrest system meets the criteria and protocols contained in Appendix C to subpart M, and if the system is being used by an employee having a combined person and tool weight of less than 310 pounds (140 kg), the system will be considered to be in compliance with the provisions of paragraph (d)(16) of this section. If the system is used by an employee having a combined tool and body weight of 310 pounds (140 kg) or more, then Company Name Here must appropriately modify the criteria and protocols of the Appendix to provide proper protection for such heavier weights, or the system will not be deemed to be in compliance with the requirements of paragraph (d)(16) of this section.

The attachment point of the body belt will be located in the center of the wearer's back. The attachment point of the body harness will be located in the center of the wearer's back near shoulder level, or above the wearer's head.

Body belts, harnesses, and components will be used only for employee protection (as part of a personal fall arrest system or positioning device system) and not to hoist materials.

Personal fall arrest systems and components subjected to impact loading will be immediately removed from service and will not be used again for employee protection until inspected and determined by a competent person to be undamaged and suitable for reuse.

Company Name Here will provide for prompt rescue of employees in the event of a fall or will assure that employees are able to rescue themselves.

Personal fall arrest systems will be inspected prior to each use for wear, damage and other deterioration, and defective components will be removed from service.

Body belts will be at least one and five-eighths (1 5/8) inches (4.1 cm) wide.

Personal fall arrest systems will not be attached to guardrail systems, nor will they be attached to hoists except as specified in other subparts of this Part.

When a personal fall arrest system is used at hoist areas, it will be rigged to allow the movement of the employee only as far as the edge of the walking/working surface.

"Positioning device systems."

Positioning device systems and their use will conform to the following provisions:

Positioning devices will be rigged such that an employee cannot free fall more than 2 feet (.9 m).

Positioning devices will be secured to an anchorage capable of supporting at least twice the potential impact load of an employee's fall or 3,000 pounds (13.3 kN), whichever is greater.

Connectors will be drop forged, pressed or formed steel, or made of equivalent materials.

Connectors will have a corrosion-resistant finish, and all surfaces and edges will be smooth to prevent damage to interfacing parts of this system.

Connecting assemblies will have a minimum tensile strength of 5,000 pounds (22.2 kN)

Dee-rings and snap hooks will be proof-tested to a minimum tensile load of 3,600 pounds (16 kN) without cracking, breaking, or taking permanent deformation.

Snap hooks will be sized to be compatible with the member to which they are connected to prevent unintentional disengagement of the snap hook by depression of the snap hook keeper by the connected member, or will be a locking type snap hook designed and used to prevent disengagement of the snap hook by the contact of the snap hook keeper by the connected member. As of January 1, 1998, only locking type snap hooks will be used.

Unless the snap hook is a locking type and designed for the following connections, snap hooks will not be engaged:

1. Directly to webbing, rope or wire rope;

2. To each other;

3. To a Dee-ring to which another snap hook or other connector is attached;

4. To a horizontal lifeline; or

5. To any object which is incompatibly shaped or dimensioned in relation to the snaphook such that unintentional disengagement could occur by the connected object being able to depress the snaphook keeper and release itself.

Positioning device systems will be inspected prior to each use for wear, damage, and other deterioration, and defective components will be removed from service.

Body belts, harnesses, and components will be used only for employee protection (as part of a personal fall arrest system or positioning device system) and not to hoist materials.

"Warning line systems."

Warning line systems [See 1926.501(b)(10)] and their use will comply with the following provisions:

The warning line will be erected around all sides of the roof work area.

When mechanical equipment is not being used, the warning line will be erected not less than 6 feet (1.8 m) from the roof edge.

When mechanical equipment is being used, the warning line will be erected not less than 6 feet (1.8 m) from the roof edge which is parallel to the direction of mechanical equipment operation, and not less than 10 feet (3.1 m) from the roof edge which is perpendicular to the direction of mechanical equipment operation.

Points of access, materials handling areas, storage areas, and hoisting areas will be connected to the work area by an access path formed by two warning lines.

When the path to a point of access is not in use, a rope, wire, chain, or other barricade, equivalent in strength and height to the warning line, will be placed across the path at the point where the path intersects the warning line erected around the work area, or the path will be offset such that a person cannot walk directly into the work area.

Warning lines will consist of ropes, wires, or chains and supporting stanchions erected as follows:

1. The rope, wire, or chain will be flagged at not more than 6-foot (1.8 m) intervals with high-visibility material;

2. The rope, wire, or chain will be rigged and supported in such a way that its lowest point (including sag) is no less than 34 inches (.9 m) from the walking/working surface and its highest point is no more than 39 inches (1.0 m) from the walking/working surface;

3. After being erected, with the rope, wire, or chain attached, stanchions will be capable of resisting, without tipping over, a force of at least 16 pounds (71 N) applied horizontally against the stanchion, 30 inches (.8 m) above the walking/working surface, perpendicular to the warning line, and in the direction of the floor, roof, or platform edge;

4. The rope, wire, or chain will have a minimum tensile strength of 500 pounds (2.22 kN), and after being attached to the stanchions, will be capable of supporting, without breaking, the loads applied to the stanchions as prescribed in paragraph (f)(2)(iii) of this section; and

5. The line will be attached at each stanchion in such a way that pulling on one section of the line between stanchions will not result in slack being taken up in adjacent sections before the stanchion tips over.

No employee will be allowed in the area between a roof edge and a warning line unless the employee is performing roofing work in that area.

Mechanical equipment on roofs will be used or stored only in areas where employees are protected by a warning line system, guardrail system, or personal fall arrest system.

"Controlled access zones."

Controlled access zones [See 1926.501(b)(9) and 1926.502(k)] and their use will conform to the following provisions.

When used to control access to areas where leading edge and other operations are taking place the controlled access zone will be defined by a control line or by any other means that restricts access.

When control lines are used, they will be erected not less than 6 feet (1.8 m) nor more than 25 feet (7.7 m) from the unprotected or leading edge, except when erecting precast concrete members.

When erecting precast concrete members, the control line will be erected not less than 6 feet (1.8 m) nor more than 60 feet (18 m) or half the length of the member being erected, whichever is less, from the leading edge.

The control line will extend along the entire length of the unprotected or leading edge and will be approximately parallel to the unprotected or leading edge.

The control line will be connected on each side to a guardrail system or wall.

When used to control access to areas where overhand bricklaying and related work are taking place:

The controlled access zone will be defined by a control line erected not less than 10 feet (3.1 m) nor more than 15 feet (4.5 m) from the working edge.

The control line will extend for a distance sufficient for the controlled access zone to enclose all employees performing overhand bricklaying and related work at the working edge and will be approximately parallel to the working edge.

Additional control lines will be erected at each end to enclose the controlled access zone.

Only employees engaged in overhand bricklaying or related work will be permitted in the controlled access zone.

Control lines will consist of ropes, wires, tapes, or equivalent materials, and supporting stanchions as follows:

1. Each line will be flagged or otherwise clearly marked at not more than 6-foot (1.8 m) intervals with high-visibility material.

2. Each line will be rigged and supported in such a way that its lowest point (including sag) is not less than 39 inches (1 m) from the walking/working surface and its highest point is not more than 45 inches (1.3 m) [50 inches (1.3 m) when overhand bricklaying operations are being performed] from the walking/working surface.

3. Each line will have a minimum breaking strength of 200 pounds (.88 kN).

On floors and roofs where guardrail systems are not in place prior to the beginning of overhand bricklaying operations, controlled access zones will be enlarged, as necessary, to enclose all points of access, material handling areas, and storage areas.

On floors and roofs where guardrail systems are in place, but need to be removed to allow overhand bricklaying work or leading edge work to take place, only that portion of the guardrail necessary to accomplish that day's work will be removed.

"Safety monitoring systems."

Safety monitoring systems [See 1926.501(b)(10) and 1926.502(k)] and their use will comply with the following provisions:

Company Name Here will designate a competent person to monitor the safety of other employees and Company Name Here will ensure that the safety monitor complies with the following requirements:

The safety monitor will be competent to recognize fall hazards;

1. The safety monitor will warn the employee when it appears that the employee is unaware of a fall hazard or is acting in an unsafe manner;

2. The safety monitor will be on the same walking/working surface and within visual sighting distance of the employee being monitored;

3. The safety monitor will be close enough to communicate orally with the employee; and

4. The safety monitor will not have other responsibilities which could take the monitor's a	attention from the monitoring function.

Mechanical equipment will not be used or stored in areas where safety monitoring systems are being used to monitor employees engaged in roofing operations on low-slope roofs.

No employee, other than an employee engaged in roofing work [on low-sloped roofs] or an employee covered by a fall protection plan, will be allowed in an area where an employee is being protected by a safety monitoring system.

Each employee working in a controlled access zone will be directed to comply promptly with fall hazard warnings from safety monitors.

"Covers."

Covers for holes in floors, roofs, and other walking/working surfaces will meet the following requirements:

Covers located in roadways and vehicular aisles will be capable of supporting, without failure, at least twice the maximum axle load of the largest vehicle expected to cross over the cover.

All other covers will be capable of supporting, without failure, at least twice the weight of employees, equipment, and materials that may be imposed on the cover at any one time.

All covers will be secured when installed so as to prevent accidental displacement by the wind, equipment, or employees.

All covers will be color coded or they will be marked with the word "HOLE" or "COVER" to provide warning of the hazard.

Note: This provision does not apply to cast iron manhole covers or steel grates used on streets or roadways.

"Protection from falling objects."

Falling object protection will comply with the following provisions:

1. Toe boards, when used as falling object protection; will be erected along the edge of the overhead walking/working surface for a distance sufficient to protect employees below.

2. Toe boards will be capable of withstanding, without failure, a force of at least 50 pounds (222 N) applied in any downward or outward direction at any point along the toe board.

3. Toe boards will be a minimum of 3 1/2 inches (9 cm) in vertical height from their top edge to the level of the walking/working surface. They will have not more than 1/4 inch (0.6 cm) clearance above the walking/working surface. They will be solid or have openings not over 1 inch (2.5 cm) in greatest dimension.

Where tools, equipment, or materials are piled higher than the top edge of a toe board, paneling or screening will be erected from the walking/working surface or toe board to the top of a guardrail system's top rail or mid rail, for a distance sufficient to protect employees below.

Guardrail systems, when used as falling object protection, will have all openings small enough to prevent passage of potential falling objects.

During the performance of overhand bricklaying and related work:

No materials or equipment except masonry and mortar will be stored within 4 feet (1.2 m) of the working edge.

Excess mortar, broken or scattered masonry units, and all other materials and debris will be kept clear from the work area by removal at regular intervals.

During the performance of roofing work:

Materials and equipment will not be stored within 6 feet (1.8 m) of a roof edge unless guardrails are erected at the edge.

Materials which are piled, grouped, or stacked near a roof edge will be stable and self-supporting.

Canopies, when used as falling object protection, will be strong enough to prevent collapse and to prevent penetration by any objects which may fall onto the canopy.

"Fall protection plan."

This option is available only to employees engaged in leading edge work, precast concrete erection work, or residential construction work (See 1926.501(b)(2), (b)(12), and (b)(13)) who can demonstrate that it is infeasible or it creates a greater hazard to use conventional fall protection equipment. The fall protection plan must conform to the following provisions.

The fall protection plan will be prepared by a qualified person and developed specifically for the site where the leading edge work, precast concrete work, or residential construction work is being performed and the plan must be maintained up to date.

Any changes to the fall protection plan will be approved by a qualified person.

A copy of the fall protection plan with all approved changes will be maintained at the job site.

The implementation of the fall protection plan will be under the supervision of a competent person.

The fall protection plan will document the reasons why the use of conventional fall protection systems (guardrail systems, personal fall arrest systems, or safety nets systems) is infeasible or why their use would create a greater hazard.

The fall protection plan will include a written discussion of other measures that will be taken to reduce or eliminate the fall hazard for workers who cannot be provided with protection from the conventional fall protection systems. For example, Company Name Here will discuss the extent to which scaffolds, ladders, or vehicle mounted work platforms can be used to provide a safer working surface and thereby reduce the hazard of falling.

The fall protection plan will identify each location where conventional fall protection methods cannot be used. These locations will then be classified as controlled access zones and Company Name Here must comply with the criteria in paragraph (g) of this section.

Where no other alternative measure has been implemented, Company Name Here will implement a safety monitoring system in conformance with 1926.502(h).

The fall protection plan must include a statement which provides the name or other method of identification for each employee who is designated to work in controlled access zones. No other employees may enter controlled access zones.

In the event an employee falls, or some other related, serious incident occurs, (e.g., a near miss) Company Name Here will investigate the circumstances of the fall or other incident to determine if the fall protection plan needs to be changed (e.g. new practices, procedures, or training) and will implement those changes to prevent similar types of falls or incidents.

"Training Program."

Company Name Here will provide a training program for each employee who might be exposed to fall hazards. The program will enable each employee to recognize the hazards of falling and will train each employee in the procedures to be followed in order to minimize these hazards.

Company Name Here will assure that each employee has been trained, as necessary, by a competent person qualified in the following areas:

1. The nature of fall hazards in the work area;

2. The correct procedures for erecting, maintaining, disassembling, and inspecting the fall protection systems to be used;

3. The use and operation of guardrail systems, personal fall arrest systems, safety net systems, warning line systems, safety monitoring systems, controlled access zones, and other protection to be used;

4. The role of each employee in the safety monitoring system when this system is used;

5. The limitations on the use of mechanical equipment during the performance of roofing work on low-sloped roofs;

6. The correct procedures for the handling and storage of equipment and materials and the erection of overhead protection; and

7. The role of employees in fall protection plans;

The standards contained in this subpart.

"Certification of training."

Company Name Here will verify compliance with paragraph (a) of this section by preparing a written certification record. The written certification record will contain the name or other identity of the employee trained, the date(s) of the training, and the signature of the person who conducted the training or the signature of Company Name Here. If Company Name Here relies on training conducted by another employer or completed prior to the effective date of this section, the certification record will indicate the date Company Name Here determined the prior training was adequate rather than the date of actual training.

The latest training certification will be maintained.

"Retraining."

When Company Name Here has reason to believe that any affected employee who has already been trained does not have the understanding and skill required by paragraph (a) of this section, Company Name Here will retrain each such employee. Circumstances where retraining is required include, but are not limited to, situations where:

1. Changes in the workplace render previous training obsolete; or

2. Changes in the types of fall protection systems or equipment to be used render previous training obsolete; or

3. Inadequacies in an affected employee's knowledge or use of fall protection systems or equipment indicate that the employee has not retained the requisite understanding or skill.

“Accident Investigation”

All accidents and serious incidents (near misses) must be investigated, implementing changes to the fall protection plan as necessary.

“Other standards”

When purchasing equipment and raw materials for use in fall protection systems, applicable ANSI & ASTM requirements should be met.